## Slide 2
Isoleren
Insulated Metal Wall and Roof Panels
Isoleren
Insulated Metal Wall and Roof Panels

## Slide 3
What are IMPs?
  Insulated Metal Panels, or IMPs, are premier building products on the leading edge of innovation. The panels are formed by a continuously, foamed-in-place manufacturing process which binds interior and exterior single-skin steel panels to a polyisocyanurate foam core. With exceptional insulating values, architectural flexibility, ease of installation and green building properties, IMPs meet the needs of a variety of building projects.

## Slide 4
Applications
Applications of IMPs are extremely diverse and often include distribution warehouses, schools, universities, aircraft hangars, hospitals, public works buildings, office buildings, manufacturing facilities, cold storage sites, maintenance buildings, car dealerships, sports complexes, churches and residential applications.

## Slide 5
Exterior Profiles
    4 Lined - ML, SL, WL, VL (Interior Profile, ML)
Notes: ML – lightly corrugated, ribbed, Mesa profile
SL – fluted, most dramatic profile (resembles reversed-rolled U-panel)
WL – striated, very small corrugated profile
VL – Micro-beads or pencil ribs

## Slide 6
Exterior Profiles
    3 Textured - IM, ST, IN (Interior Profile, ML)
    1 Roof - RL (Interior Profile, ML)
    1 Specialty (Fire Rated) - MF, VF, SF (Interior Profile, ML)
Notes: IM – flat, heavy embossed
ST – flat, embossed
IN – flat, smooth
RL – standing seam, lightly corrugated, ribbed, Mesa profile
Isoleren Fire Rated – Available in MF, VF, SF profiles

## Slide 7
Product Information
  Gauge - 26, 24, 22
    Gauge based on profile, texture and performance requirements
  Thickness - 2", 2.5", 3", 4", 5", 6"
    2" to 3“ - commercial/industrial/institutional
    4" to 6“ - cold storage
  Width - 42", 36", 30“
    Width based on vertical/horizontal application and profile
  Length - 8' min, 53‘ max (12’ roof)
    Length based on vertical/horizontal application and profile
  Texture - smooth or embossed
  Colors – 7 wall colors, 5 roof colors unique to Isoleren
    Exterior - PVDF, Interior: Polyester
  Metal - Steel
  Core - Continuously poured-in-place, polyisocyanurate, insulating foam

## Slide 8
Product Information
Uncoiler section
Roll formers – liner/facer
Foaming section
Curing oven
Band saw
Stacking/staging area
Packing/shrink wrapping

## Slide 9
  Single component wall assembly
    Faster installs, fewer fasteners, fewer structural supports, all weather conditions except high winds
  Vapor and Air Infiltration
    Properly sealed system required
    Non-skinning butyls used on perimeter and all joints
    Creates air/vapor barrier
  Drainage wall assembly
    Single component assembly for use with exterior single skin facade
  Trim and accessories available
Installation
Non-skinning butyl
(optional)
Continuous non-skinning
butyl sealant

## Slide 10
Installation
Install clips and screws at all intermediate supports
Secure top of panel with clips and screws
Plumb panel with level
Secure bottom of panel with clips and screws
Align panel edge with corner line
Corner panel
Secure edge of panel with self-drilling screws

## Slide 11
Installation
SEALANT PIGTAIL
Eave/Rake framing
Marry non-skinning butyl caulk together at panel to eave/rake member form airtight seal
Non-skinning butyl caulk
Insulated wall panel
SEALANT PIGTAIL
Base attachment angle (by others)
Urethane sealant
Marry non-skinning butyl caulk to urethane sealant at base of panel to form airtight seal
Insulated wall panel
Non-skinning butyl caulk
Cover trim
Base trim
Sealant tape

## Slide 12
Installation
Slide panel over to fully engage joint of installed panel
Next panel
Push bottom of panel to engage joint of installed panel
Installed panel

## Slide 13
Performance
  Single component wall assembly
    Faster installs, fewer fasteners, fewer structural supports, all weather conditions except high winds, superior spanning
  Exceptional insulating properties
    R7.25 (thermal resistance) per inch
  Sustainable
    Reduces energy consumption, metal is recycled and recyclable
  High quality
    Structural, finished interior, rigorously tested, PVDF paint finishes, warranties
  Architectural flexibility
    Lightweight, thermally efficient
    Dual uses: Primary wall component or drainage wall assembly
    Can be integrated with traditional building systems
    Various finishes, gauges, profiles and thicknesses

## Slide 14
Resources
    Product data sheets
    Color chart
    Details/Drawings
    Product specifications
    Installation manuals
    Testing
    Technical bulletins
    Warranty: panel warranty, paint warranty
  2 year blister warranty
  20 year substrate warranty
  30 year finish warranty, 20 year product warranty
  7 wall colors, 5 roof colors unique to Isoleren
    Custom colors available and are subject to longer lead times & minimum quantity requirements
  Support /Resources